## Slide 1
PROJECT PORTFOLIO · 2026
Why is one room colder?
Measuring heat loss with ESP32 sensor nodes, weather data and an RC circuit model. Plus: a closed-loop LED lamp.
Anmol Bhandohal
BSc Electrical Engineering (Co-op) · University of Alberta
Real data: Room A, Oct 3 to 4, 2026. 5,747 sensor readings; the furnace's heating sawtooth, detected automatically.

## Slide 2
THE QUESTION
Three explanations, three different fixes
2 / 17
Anmol Bhandohal · Electrical Engineering, University of Alberta
One bedroom is always colder. Before spending money on a fix, find out which of these is actually true.
H1
Less sun
Window faces away from the sun
DATA WOULD SHOW
Gap in daytime only; disappears at night
FIX
Curtains or accept
H2
Leaky envelope
Poor insulation, air leaks (low R)
DATA WOULD SHOW
Room cools faster after every furnace cycle
FIX
Weatherstrip, caulk, insulate
H3
Weak heating
Damper partly closed, long duct
DATA WOULD SHOW
Room warms less per furnace cycle
FIX
Open or balance dampers

## Slide 3
THE IDEA
A room behaves like an RC circuit
3 / 17
Anmol Bhandohal · Electrical Engineering, University of Alberta
C · dT/dt = (Tout − T) / R
+ a·solar + b·furnace
▪ Walls and air leaks = resistor R. Heat flow ∝ temperature difference, like Ohm's law.
▪ Air and furniture = capacitor C: they store heat.
▪ τ = RC is one number per room. A leaky room has smaller R, smaller τ, and cools faster.
▪ Comparing τ between rooms separates H2 from H1 and H3.

## Slide 4
APPARATUS
How it's measured
4 / 17
Anmol Bhandohal · Electrical Engineering, University of Alberta
10 s
sampling interval, temperature · RH · pressure · light
±0.2 °C
target agreement between nodes after calibration
1 min
resampled grid, joined to hourly Edmonton weather
100 %
of derived values reproducible as Excel formulas
ESP32 · Bosch BME280 · ROHM BH1750 · Arduino C++ · Python (pandas, scikit-learn) · Open-Meteo API · Microsoft Excel

## Slide 5
METHOD
The experiment, phase by phase
5 / 17
Anmol Bhandohal · Electrical Engineering, University of Alberta
0
Calibrate
Both nodes side by side for 24 h. Measure the offset, subtract it everywhere.
Pending
1
Baseline
One node in Room A. Build and test the whole pipeline on real data.
Done
2
Two rooms
One node per room, 1.2 m high, away from vents. Log events.
2 to 3 weeks
3
Analyse
τ per room, rise per furnace cycle, day vs night, wind.
Pipeline ready
Why calibrate first: each sensor is only ±1 °C accurate out of the box, which is bigger than the effect being measured.

## Slide 6
RESULTS · MEASURED
Night 1: the room, the weather and the furnace
6 / 17
Anmol Bhandohal · Electrical Engineering, University of Alberta
18.9 °C
average room temperature
2.7 → 16.9 °C
outdoor range
23.9 h
Room A time constant τ (RC fit)
The thermostat holds about 19 °C while it drops to 2.7 °C outside.
τ ≈ 24 h: with the furnace off, Room A would lose about 0.8 °C in the first hour.

## Slide 7
RESULTS · MEASURED
9 furnace cycles, found automatically
7 / 17
Anmol Bhandohal · Electrical Engineering, University of Alberta
Chart: Temperature rise per heating cycle (°C)
| #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9
Rise per cycle (°C) | 0.35 | 0.31 | 0.38 | 0.42 | 0.42 | 0.44 | 0.49 | 0.52 | 0.94
0.48 °C
average rise per cycle
56 min
average time between cycles
≈ 20 min
furnace on-time per cycle
Method: smooth over 5 min, find where dT/dt changes sign, keep rises ≥ 0.15 °C (15× the sensor resolution).

## Slide 8
EXTENSION · MEASURED
Can ML forecast the room 30 minutes ahead?
8 / 17
Anmol Bhandohal · Electrical Engineering, University of Alberta
Chart: Mean absolute error, 5-fold time-series cross-validation (lower is better)
| Persistence (baseline) | Ridge regression | Gradient-boosted trees
MAE (°C) | 0.187 | 0.273 | 0.179
HONEST RESULT
▪ Best model beats "no change" by only 4.7 %, and loses on a single hold-out split.
▪ One night holds just 9 furnace cycles. The model needs weeks of data.
▪ Tested so it never trains on the future (time-series folds).
Features: recent temperature changes, indoor–outdoor gap, solar radiation. Python + scikit-learn.

## Slide 9
RESULTS · DATA COLLECTION IN PROGRESS
Room A vs Room B: the actual experiment
9 / 17
Anmol Bhandohal · Electrical Engineering, University of Alberta
PENDING DATA
What gets computed per room
Metric | Room A | Room B
Time constant τ (h) | 23.9 | ?
Rise per furnace cycle (°C) | 0.48 | ?
Cooling rate per °C ΔT (1/h) | 0.063 | ?
Day − night gap (°C) | ? | ?
Every chart, table and formula is already built. Room B's logs get pasted into the workbook and the results fill in.

## Slide 10
INTERPRETATION
Decision rules, written before the data arrives
10 / 17
Anmol Bhandohal · Electrical Engineering, University of Alberta
τ(B) at least 25 % smaller than τ(A), day and night
→
H2 · leaky envelope
Weatherstrip, seal outlets on exterior walls
Similar τ, but B warms clearly less per cycle
→
H3 · weak heating
Open or balance dampers, check the duct
Gap mostly in daytime; B's light curve peaks late or low
→
H1 · less sun
Accept, or thermal curtains at night
Gap grows with wind speed
→
Air leaks (part of H2)
Air-seal first: the cheapest fix
Fixing the rules first stops me from bending the result toward the answer I expected.

## Slide 11
ADAPTIVE LED LAMP · MEASURED
Project 2: is the LED lamp's dimming linear?
11 / 17
Anmol Bhandohal · Electrical Engineering, University of Alberta
Chart: PWM duty cycle (%)
| 10.0 | 20.0 | 30.0 | 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0 | 100.0
Measured plateau mean | 25.9 | 51.26 | 78.33 | 103.73 | 130.7 | 156.28 | 180.6 | 208.64 | 232.96 | 260.74
Fit: 2.602 lx/% (R² = 0.99991) | -0.19 | 260
0.99991
R², light vs duty
0.51 %
worst deviation from the line (of full scale)
7×
finer sensor resolution after fixing the first failed test
ESP32 · IRLZ44N MOSFET · 12 V strip · BH1750

## Slide 12
ADAPTIVE LED LAMP · MEASURED
Holding a set brightness with feedback
12 / 17
Anmol Bhandohal · Electrical Engineering, University of Alberta
u ← u + (G/K)·error
▪ Integral controller, gain G = 0.35
▪ Plant gain K measured by the lamp itself, since it changes with sensor position
▪ Simulated first: stable even with K wrong by 2×
▪ 3.5 s to settle at 11 lx, 0.21 lx overshoot, ±0.1 lx ripple

## Slide 13
ADAPTIVE LED LAMP · MUSIC-REACTIVE MODE
Then I made it react to music
13 / 17
Anmol Bhandohal · Electrical Engineering, University of Alberta
0 mics
it listens to the audio stream itself, so headphones work and room noise is ignored
60 fps
brightness updates, sent over serial to the ESP32's PWM
140 ms
Bluetooth delay measured and compensated, so flashes land on the beat
Same lamp hardware as before. The music mode is a Python engine on the PC: numpy FFT, auto gain control, onset detection.

## Slide 14
ADAPTIVE LED LAMP · DESIGN DECISIONS
Four versions, judged against an independent beat tracker
14 / 17
Anmol Bhandohal · Electrical Engineering, University of Alberta
v1
Mapped raw volume. Swung only 50–70 % and followed the volume knob, not the music.
v2
Auto gain over an 8 s window, so it works at any volume.
v3
Kick detector tuned on a synthetic track. On real songs it caught only 0.12–0.33 kicks per beat.
v4
Continuous bass/mid onset strength: 5.8× the beat contrast on the same song.
Chosen: mellow. Picked by watching all three v4 styles on the same song. It keeps the room lit (58 %) and still lands the beats.

## Slide 15
ADAPTIVE LED LAMP · VIDEO
Watch it
15 / 17
Anmol Bhandohal · Electrical Engineering, University of Alberta
Real lamp, behind the monitor (click to play)
Rendered comparison: the three v4 styles run on the same 30 s of music. Left: simulated diffuser at the commanded brightness. Right: brightness trace with detected hits.

## Slide 16
CONCLUSIONS
What I built, and what's next
16 / 17
Anmol Bhandohal · Electrical Engineering, University of Alberta
Done
▪ Sensor → ESP32 → Wi-Fi → Python → Excel chain, validated on 16 h of real data
▪ Room A: 9 furnace cycles, ≈ 0.5 °C each, τ ≈ 24 h
▪ LED lamp: linear to R² 0.9999, closed-loop control within 1 sensor count
▪ Music mode: 4 versions, judged against librosa; v4 has 5.8× the beat contrast
Next
▪ Build node 2 and run the 24 h side-by-side calibration
▪ Log both rooms for 2 to 3 weeks
▪ Fill in the comparison and apply the decision rules
The same approach transfers to any building or equipment question: measure, model, then decide.

## Slide 17
Thank you
Anmol Bhandohal · bhandoha@ualberta.ca
linkedin.com/in/anmol-bhandohal-904789305
Technical report (Word)
Analysis workbook (Excel)
Firmware + Python code
available on request